Extension and Evaluation of a Sequence Detection System in Wireless Sensor Networks

---
Intension
- Large scaled sensor networks
  - Sequence/Location is important
- Dynamically detect sequence of sensor modules
  - Measurement data can be bound to location

---
System overview 1
Node 1
Node 2
Node 3
Node 4
- Each node transmit broadcast
  - Other nodes measure RSS
- Transmit on several frequencies for precision
- Measurment data processing

---
System overview 2
Node 1
Master Node
Node 2
Node 3
Node 4
- Data collection to master node
- Processing data/measurements
  - Either on node
  - Or on connected PC
- Send results to PC

---
Current implementation
- Developed by Onur Ergin
- Based on TinyOS and “tmote” sensor modules
- Dynamically detect and handle nodes in range
- Limitations
  - Own data collection protocol doesn't perform well
  - System not intended for larger sensor meshes
  - Slow in larger networks due to waiting

---
Project Plan
- Based on TinyOS and “tmote” sensor modules
- Coding from scratch
- Improvements/Extesion to old code
  - Use standardized protocols
    - CTP
    - Dissemination
  - Try to improve wait times for faster measurements
    - Especially on large sensor meshes

---
Hardware
- Microprocessor
- Sensors
  - For measurement
- 802.15.4 Wireless
  - Several frequencies
- USB
  - Easy programming
  - Simple serial access